## Slide 1: Biologically Inspired Turn Control for Autonomous Mobile Robots
Xavier Perez-Sala, Cecilio Angulo, Sergio Escalera

## Slide 2: Motivation

## Slide 3: Motivation
Path planning
Robot navigation
Path execution
Unexpected behaviour
Path execution control is needed !

## Slide 4: Overview
General path execution control
Turn control
Only using: Camera images + “neck” sensor
Without: Artificial landmarks, egomotion
Consecutive frames  Motion information
Successfully tested on Sony Aibo

## Slide 5: Biological inspiration
Goal Oriented Human Motion
3-4 years:
Head stabilization
4-6 years:
Egocentric representation of the environment
7-8 years:
Landmarks  Intermediate
goals
9-10 years:
Exocentric representations
Anticipatory movements
Mobile Robotics
Artificial vestibular systems
Odometry, Egomotion...
Navigation using landmarks
SLAM
This work!

## Slide 6: Biological inspiration
Goal Oriented Human Motion
3-4 years:
Head stabilization
4-6 years:
Egocentric representation of the environment
7-8 years:
Landmarks  Intermediate
goals
9-10 years:
Exocentric representations
Anticipatory movements
Mobile Robotics
Artificial vestibular systems
Odometry, Egomotion...
Navigation using landmarks
SLAM
This work!

## Slide 7: Turn Control (I)
Initial Stage
Head rotation to the desired angle (Set point)
Body-head alignment (body control + head control)
Final orientation (Body and head aligned)

## Slide 8: Turn Control (II)
Body-Head alignment
Rotation Angle
SURF flow

## Slide 9: Body-Head alignment
Body-Head alignment
Rotation Angle
SURF flow

## Slide 10: Body-Head alignment
Body Control
Head Control
Set point: Maintain head orientation
Action: “Pan” angle θ
Error: Instantaneous head rotation ϕ
Set point: Align the neck
Action: Walk velocity
Error: “Pan” angle θ
Notes: Body Control rotates the whole robot

## Slide 11: Rotation Angle
Body-Head alignment
Rotation Angle
SURF flow

## Slide 12: Rotation Angle (I)
Motion field:
Projection of 3-D relative velocity vectors of the
scene points onto the 2-D image plane
Pure rotations:
Vectors show the image distortion due to camera
rotation
Notes: The motion field has a parabolic non-linearity, which is due to perspective  Parallel vectors of the same length

## Slide 13: Rotation Angle (II)
Optical flow:
2-D displacements of brightness patterns in the
image
Optical flow = Motion field ?

## Slide 14: Rotation Angle (III)
Restriction:
Rotation axis match the image plane
Robot (Sony Aibo):
Rotation involves a small translation
Assumption:
Pure rotation + noise in the measure
Notes: Rotation involves a translation of the camera

## Slide 15: Rotation Angle (IV)

## Slide 16: SURF Flow
Body-Head alignment
Rotation Angle
SURF flow

## Slide 17: SURF Flow(I)
Optical flow restrictions:
Brightness constancy
Temporal persistence
Spatial coherence

## Slide 18: SURF Flow(II)
Corner detection
SURF description & selection
Correspondences
Parallel vectors
Mean length & mean angle

## Slide 19: SURF Flow(III)
Correspondences:
Refinement:

## Slide 20: Experiments
Rotation angle
Robot turning
Robot: Sony Aibo ERS-7
PC - robot processing (wireless)
Sampling time: 100ms
Rotation measured using a zenithal camera

## Slide 21: Rotation Angle

## Slide 22: Rotation Angle
Maximum rotation/sampling time = 3º

## Slide 23: Robot turning
Specific software:
General approach:

## Slide 24: Results

## Slide 25: Straight Forward (I)

## Slide 26: Straight Forward (II)

## Slide 27: Conclusions
Only camera images and neck sensor are used
Biologically inspired navigation
Without artificial landmarks or egomotion
Similar results that to specific system
  Rotations > 15º
Exportable system
Problems with wireless connection

## Slide 28: Future work
Test on other platforms
Correct robot trajectory using motor information
Sampling rate decreasing

## Slide 29: Thanks for your attention
Questions?